# PDF Encryption Spec Draft
## Draft spec/comments
The following few lines are a short comment regarding the implementation of encryption in PDF export filter. I wrote this with PDF vers. 1.4 specification and some information from PDF vers. 1.5 and 1.6 at hand.

The idea is to implement encryption according to PDF ver. 1.4, in its basic incarnation.

References:
Title	Link
OOo 2.0 PDF Export	http://specs.openoffice.org/appwide/pdf_export/PDFExport.sxw
OOo 2.0.3 PDF Export Dialog	http://specs.openoffice.org/appwide/pdf_export/PDFExportDialog.odt
PDF Reference / third edition / Adobe Portable Document Format / Version 1.4	The PDF specification, version 1.4 from Adobe.

## Intro
A PDF file can be encrypted to protect its content from unauthorized access.
The various aspect of the encryption and access control in a viewer are implemented through a software module called security handler.
There can be different security handler implementations, among them:
- Standard security handler. It permits access permissions and two passwords for a documents.
- Publick key security handler. In this case the public key technology is used to encrypt a document and it's possible to specify a list of recipients, each list have its own access permissions. In this every list of recipients can be associated to different acces permissions.
- Crypt filters (only PDF vers. 1.6). They permit a finer granularity over the document encryption. Every single stream can have its own filter.
## Implementation
It's my opinion that currently only the Standard security handler should be implemented, for the following reasons:
- it gives two passwords protection with access permissions, sufficient for most uses;
- the building blocks needed (MD5 digest, ARCFOUR cypher, the AES as available on PDF v.1.6 is not yet available on OOo source tree) are already present in OOo;
- the consumer applications (that is, the viewers) are all expected to support the Standard security handler;
- from what I'm seeing in issues 12626 and the other duplicates of it, it's what users request.
- it was relatively simple to implement in OOo ( meaning that as of today I've already done most of the “grunt” work needed ).
- keeping it to PDF v1.4, only ARCFOUR (RC4 compatible) encryption is provided.

For a detailed description of the encryption implementation, please see chapter 3.5 of PDF specification version 1.4.
## Some words on the passwords
Implementing standard security means giving two access level: owner and user and two different passwords, one for the owner permission level, the other for the user level.
The owner is defined as the person who can change the document permissions, the user is defined as the person who can only “see” the document if he/she knows the user password.

The PDF specs don't say anything about the passwords: you can leave the passwords blank (empty), I think that the encryption without at least the owner password is meaningless: you end up with a PDF document with fixed permission, that can be changed simply by giving an empty owner password to the application used to edit the PDF.
May be it's something that can be left to the user, a decision wether this PDF implementation permits empty owner password should be made.

If the user password is left blank, than no user password will be needed to open the PDF, but the owner password will still be needed to change the permissions.
That means a PDF file that can be opened by everyone.

The encryption is done “on the fly”, that is while exporting the file is encrypted; this may lead to a longer saving time when the file is saved as encrypted PDF compared to the non encrypted one, especially with huge files.
## UI
The UI is basically built adding a tab to the dialog as it is in OOo 2.0.3.
A first proposal is in the following illustration.

Illustration 1: PDF Export dialog security page, snapshot, draft
The Activate encryption checkbox activates/deactivates all the others.
The following table shows how.

Type	Properties	Notes/comment
Tab page name	String en_US: Security
Check box	String en_US: Activate encryption / Enabled: yes, always / Initially marked: no	Main selection to enable password encryption. / Activates/deactivates all the remaining items.
Edit text	String en_US: Owner password / Enabled: only if Activate encryption is active / Initial state: empty	this needs reworking, a double request on the input should be done. See following lines, at the end of the table.
Edit text	String en_US: User password / Enabled: only if Activate encryption is active / Initial state: empty	Same observation as above.
Fixed line	String en_US: Low level security options / Enabled: only if Activate encryption is active / Initial state: N/A	section title
Check box	String en_US: Printing / Enabled: only if Activate encryption is active / Initial state: yes	When selected the user can print the PDF file, always at high resolution. See Printing permissions
Check box	String en_US: Document changing and assembly / Enabled: only if Activate encryption is active / Initial state: no	Modify the content of the document
Check box	String en_US: Content extract for copying and accessibility support / Enabled: only if Activate encryption is active / Initial state:	Copy or extract text and graphics from the document, in support for accessibility or other purposes.
Check box	String en_US: Commenting, form filling and signing / Enabled: only if Activate encryption is active / Initial state:	Add or modify text annotation
Check box	String en_US: High level security (128 bit) / Enabled: only if Activate encryption is active / Initial state:	Enables high security level encryption, treated as Revision 3 in this impementation.
Fixed line	String en_US: High level security options / Enabled: only if Activate encryption and High level security are both active / Initial state: N/A	section title
Check box	String en_US: Fill form and signing / Enabled: only if Activate encryption and High level security are both active / Initial state: no	Fill in interactive form fields, even if “Commenting, form filling and signing” above is unselected.
Check box	String en_US: Extraction for accessibility / Enabled: only if Activate encryption and High level security are both active / Initial state: no	Extract text and graphics (in support of accessibility / to disabled users or for other purposes). This even when
Check box	String en_US: Document assembly / Enabled: only if Activate encryption and High level security are both active / Initial state: no	Assemble the document: insert, rotate and/or delete pages, even if “Document changing and assembly” above is unselected.

### Notes
- the password should need a double input, to confirm.
- how the passwords are saved in config ? Encrypted ? How ?

The options activated when high level encryption is selected are valid in their own; that is you can have a PDF file that can be printed, the content extracted for accessibility, but not copied or extracted to paste the content elsewhere.
### Printing permissions
There is a permission selection that should result in high or low resolution printing enable.
This behavior is honored by Acrobat reader only when printing in Windows. On Unix system the Acro reader prints only in high resolution, the behavior in Mac system is unknown to me. (see Appendix H, note 16 on PDF ref. V. 1.4 )
The High/Low resolution printing behavior is not honored at all by xpdf, gpdf and kpdf. That is they print always in high resolution, whatever the selection.
My suggestion is that printing, if enabled, will always be at high resolution.
## Configuration
Will be provided as soon as I'll have the English strings frozen, I'd like to use a similar text for the configuration item names.